Real-time communication and collaboration

System Design:

Client1
Client2
Client3
Server

1.Send coordinates and color of cube
2. Send modified coordinates and color
2. Send modified coordinates and color

Protocols:
Client-Server architecture will be used.
Multiple users can view and modify the cube simultaneously.
When a client changes the color of a side of the cube, the coordinates(X,Y, Z) and color(R, G, B) will be sent to server and modified values will be stored in redis. The server will then send the changes to other clients, in real time, so that they can view the changes.

Suggested Library / Stack : Socket.IO, Redis

Expected Scalability, Availability and Fault Tolerance:
As the number of users increase(ex: thousand users simultaneouly) and the data increases, it will cause a lot of load on server.

So when our application attracts more users and our server reaches its maximum load we will need to split connections over multiple servers.

Risks:
Socket.IO is built on asynchronous networking libraries. If clients start sending significant amounts of data via Socket.IO, it streams data in chunks. This will cause load on server.